A110 E-TERNITÉ: VOLLEDIG ELEKTRISCH PROTOTYPE VOL GEAVANCEERDE ALPINE-INNOVATIE

21/07/2022

- Werelddebuut van volledig elektrische Alpine A110 E-ternité bij Franse Grand Prix.

- Alpine viert 60e verjaardag van de A110 met een prototype vol ‘Made in Alpine’-innovaties en geeft een blik in de toekomst van het merk.

- Alpine A110 E-ternité is een rijdend laboratorium voor een volledig elektrische open sportauto met de legendarische wendbaarheid van Alpine, dankzij ongekend laag gewicht voor een elektrische auto in dit segment!

“Ik wil Alpine elektrificeren om zo de naam voor de eeuwigheid te behouden.”

Deze zin, door Luca de Meo uitgesproken kort na zijn komst bij Renault Group, inspireerde direct zowel Laurent Rossi, CEO van Alpine, als de ingenieurs van het merk. Binnen een jaar bracht het vastberaden team dit idee tot werkelijkheid. Bovendien maakte het gelijk van de gelegenheid gebruik om het dak van de A110 gedeeltelijk te verwijderen.

De volledig elektrische Alpine A110 E-ternité is het resultaat van het verkenningswerk van het team van Alpine-ingenieurs. Dit prototype is mooi op tijd voor de viering van de 60e verjaardag van de klassieke A110. De A110 E-ternité slaat een brug tussen een prestigieus verleden en een volledig elektrische toekomst en illustreert het werk dat Alpine momenteel verricht aan de ontwikkeling van zijn nieuwe modellen.

EEN ONMOGELIJKE UITDAGING?

Al meer dan tien jaar lang is Renault Group een pionier op het gebied van elektrische auto’s. De groep beschikt over een zeer rijke ervaring op alle gebieden van de automotive industrie. Het ligt dan ook voor de hand dat het team van Alpine al vroeg over elektrificatie nadacht.

De komst van Luca de Meo en zijn aankondiging van de elektrificatie gaf het team een duidelijke richting en de kans om op een verkennende manier aan elektronica te werken. In de geest van een ‘restomod’ vormde de A110 het ideale platform voor dit onderzoekswerk. Het model slaat een brug tussen een ambitieus verleden en een nog ambitieuzere toekomst.

Het doel is dus duidelijk: het elektrificeren van de nieuwe generatie Alpine-modellen. Waarom dan niet beginnen met de A110? Dat is immers het toonbeeld van sportiviteit met zijn lage gewicht en grote wendbaarheid – en dat voor een realistisch budget.

“Een niet op te lossen tegenstrijdigheid”, volgens sommigen; “een uitdaging die Alpine aankan”, volgens het gepassioneerde team van het merk.

TECHNOLOGY AND INNOVATION AT THE CORE OF THE PROJECT

The mandate was simple: electrify the A110 and match the performance, balance and agility of the Alpine A110 combustion engine car while capitalizing on the Group's strengths, experience and technologies.

To spice up this challenge a little more, Alpine is going to add four innovations to the mandate:

- an innovative multimedia system using the driver's personal tablet for an intuitive and natural connectivity experience, based on Google or Android, allowing all the user's applications to be centralised on a single device

- a state-of-the-art audio system with 8 speakers to recreate surround sound.

- innovative materials to combine performance and sustainability

- a "top-off" solution that allows you to enjoy the quietness of the electric technology: a dream to drive an electric Alpine A110 in the open, without a sound.

THE CHALLENGES OF THE DRIVETRAIN

- A DRIVE TRAIN AND BATTERY MODULES FROM THE GROUP

As a Renault Group brand, it was natural, for this new project, to look first at the parts and technologies already available in-house. The battery modules are identical to those of the 100% electric Mégane E-Tech. However, to achieve optimum weight distribution and to accommodate the twelve battery modules, it was necessary to design specific battery casings for the A110 and to adapt the internal architecture. Four modules were therefore placed at the front and eight at the rear. To meet this challenge, the engineers allowed themselves to position these modules in the space in a ‘atypical’ fashion.

Despite the addition of these twelve modules, the total weight of the Alpine A110 E-ternité remains particularly light with an increase of only 258 kg, thanks to a contained mass for the battery pack (392 kg).

- A GEARBOX SPECIFICALLY DEVELOPPED BY ALPINE

In order to get away from the 0 to 100kph / top speed trade-off and the constant quest for electric storage that requires large batteries, an innovative gearbox was added to the Group’s “standard” motor.

No gearbox available in-house allowed the Alpine engineers to meet the brief requirements of this A110 E-ternité. The desire was to find a smooth and efficient gearbox without torque breakage, but also light and compact.

A gearbox was studied in-house, with the Alpine gearbox supplier, in double clutch version (DCT) with an electronic control, as on the A110 combustion engine, but with clutches dimensioned to pass high torques. The double clutch solution makes it possible to avoid a break in torque while remaining compact and light.

- ELECTRONIC SYSTEM: A SUCCESSFUL TRANSPLANT OF TWO TECHNOLOGIES

The Alpine team showed ingenuity on the electronic system, mixing two electronic equipment architectures separated by ten years. This innovation provides new opportunities for architecture simplification or continuous improvement throughout the product as it enabled the features of the combustion engine AS1 to be kept whilst adding new features from the EV sector, as well as others such as the “Overtake” feature or the possibility of enabling communication between two batteries.

A single ECU was installed to ensure communication between the two systems. This innovation brings new opportunities for simplifying architectures or for continuous improvement throughout the product life cycle.

INNOVATIVE FEATURES

The A110 E-ternité offers even more, with new equipment developed simultaneously by the Alpine engineers.

- A LONG-AWAITED OPEN ROOF

For a long time, the demands for a convertible A110 have been heard. Alpine decided to take on one more challenge at the same time. The difficulty was above all to find the solution to quickly integrate a removable roof on the structure of the Alpine A110. The Alpine engineers thus imagined a simple and light solution, without impacting the rigidity of the production A110, with two roof shells injected with recycled carbon. A component designed and built entirely in-house.

- CENTRAL SCREEN & AUDIO SYSTEM

Alpine engineering has made it a priority to develop a vehicle that is as beautiful as it is efficient. The cockpit must therefore reflect this as well. The team succeeded in combining the design requirements with the electronic architecture ones. The solution: the wiring was done directly with the dashboard and the same interface computer was used. The result lives up to expectations and also integrates:

- a state-of-the-art audio system with 8 speakers including a subwoofer to recreate a surrounding sound.thanks to one central and two rear new speakers.

- an innovative multimedia system using the driver's personal tablet as the multimedia screen, in order to display the usual environment and apps of the user. This solution provides an always up-to-date operating system combined with the latest screen technologies.

- INNOVATIVE MATERIALS

Both lightweight and more environmentally friendly, the materials used on some key parts are made from flax. A second E-ternité prototype was also developed and displays this new technology applied to parts such as the skin of the bonnet, roof, rear window, grille, seat shells and rear skirt. The material comes from the Terre de Lin company based near Dieppe (Normandy, France). As strong as carbon-fibre and with better acoustics, flax is a material of the future.

This new experience also makes it possible to prepare for the future. Indeed, the design of the parts is now compatible with the various composite materials, which means that the same mould can be used to produce carbon, glass or flax fibre composite.

Promising research for the future!

DRIVE TRAIN AND BATTERY MODULES

TECHNICAL SPECIFICATIONS

|  | ALPINE A110 ICE | A110 E-TERNITÉ |
| --- | --- | --- |
| PERFORMANCES |
| Maximum torque | 320/340 Nm | 300Nm |
| Maximum Power | 215/221 kW | 178kW |
| Time for 0 to 100 kph | 4,4s / 4,2s | to 4,5 s |
| Vmax | 260/280 km/h | to 250 km/h |
| 1000 m DA | 22,8/22,4 s | 23,7 s |
| WEIGHT |
| Curb Weight | 1120 kg | 1378 kg (target 1320 kg) |
| Fr / Rr distribution | 43 / 57 | 42 / 58 |
| RANGE (60 kw/h) |
| WLTP (Km) | 550 | 420 (BCB LR/ 470) |

| Engine / e-Motor: | MR18 215kW / 320Nm | 6AM 178kW / 300Nm |
| --- | --- | --- |
| Gearbox | DCT 7 Getrag DW30 | Alpine DCT 2 |
| Gear Ratio | 7 | 2 |
| Wheel | Forged aluminium Fr:7,5J18 / Rr:8,5J18 | Forged aluminium Fr:7,5J18 / Rr:8,5J18 |
| Tyre | Fr:215/40 R18 – Rr:245/40 R18 | Fr:215/40 R18 – Rr:245/40 R18 |
| Front axle | Double whisbone | C/O A110 ICE |
| Rear axle | Double whisbone | C/O A110 ICE – lower arm reinforced |
| Spring | Fr: 47 N/mm / Rr: 90 N/mm | Fr: 50 N/mm / Rr: 130 N/mm |
| Anti roll bar | Fr: 106 daN.m/° / Rr: 29,8 daN.m/° | Fr: 106 daN.m/° / Rr: 29 daN.m/° |
| Shock absorber | Mando | Ohlins |
| E/E | T4VS | T4VS / Alpine interface / SWEET 200 |
| Battery | SO | 62 kWh/200 kW |
| MVODM | 1120 kg | 1378 kg |

PRESS CONTACTS

Orianne Tamburini

Head of product communication

orianne.tamburini@alpinecars.com

+33 6 26 63 28 14

Johanna Moreau

Press Officer

Johanna.moreau@alpinecars.com

+33 6 38 28 03 44

ABOUT ALPINE

Founded in 1955 by Jean Rédélé, the brand has set itself apart with its French-style sports cars. In 2018, the brand presented the new A110, a sports car faithful to Alpine's timeless principles of compactness, lightness, agility and driving pleasure. The Alpine Business Unit was created in 2021 and thus became the brand dedicated to innovative, authentic, exclusive sportscars of the Renault Group, benefiting from the heritage and craftsmanship of its historic plant in Dieppe and the Alpine Racing and Alpine Cars teams engineering mastery.